## Slide 1: Conducting A QSO - Phone

## Slide 2: Conducting A QSO – Phone (cont.)
Rule Number 1
  Listen
  Listen
  Listen

## Slide 3: Conducting A QSO – Phone (cont.)
Four methods to make a contact
  Call CQ
  Answer a CQ or QRZ
  Joining a QSO in progress – Break in
  Tail ending

## Slide 4: Conducting A QSO – Phone (cont.)
Calling CQ
  Listen for an open frequency
    Minimum of 3 KHz away from a signal
    After tuning the transmitter, ask if frequency is in use
    If no one responds, call CQ
    Keep it short
      “CQ CQ calling CQ this is W4XYZ, Whiskey-Four- Xray-Yankee-Zulu”
      Learn phonetics (see last slide)
      Repeat once – wait for a response

## Slide 5: Conducting A QSO – Phone (cont.)
After response, call back
  “K8ABC, Kilo-Four-Alpha-Bravo-Charlie this is W4XYZ”
  Next the essentials
    Thanks for the call back
      Signal report: 5-9, 5-8, 5-7, etc.
      Name is John – Juliet-Oscar-Hotel-November
      QTH is Bluffton, SC
    Back to you
      K8ABC this is W4XYZ

## Slide 6: Conducting A QSO – Phone (cont.)
Next Round
  Exchange call signs
    Describe station and antenna
      “I am using a Kenwood TS-480 running 100 watts to a dipole up about 40 feet”
    Now you are ready for general discussion
    Items you can talk about
      Use the other ham’s name at least once on each transmission
      Talk about being a new ham
      Ask how long he has been a ham
      Ask for any advice he can give you

## Slide 7: Conducting A QSO – Phone (cont.)
      Ask questions about his location
      Professional background
      Other hobbies you or he may have
Answering a CQ or QRZ
  Same procedure as calling CQ
  Joining a QSO in progress – Break in
  When listening to two or more hams in a discussion
    Announce your call sign once

## Slide 8: Conducting A QSO – Phone (cont.)
    When one of the hams acknowledges you
      Announce your call sign again with phonetics and your name
      Tell them you put up a new antenna and you would like a signal report
      Ask if you can join in
      Most hams are happy to have another person in the group
    Go through the same disclosures as before
Tail ending
  Wait until the QSO you are listening to is over
  Call the station you wish to talk to
    This works about half the time
    Each station may sign off or change frequency before you complete the call
    Go through the same disclosures as before

## Slide 9: Conducting A QSO – Phone (cont.)
Web Sites for operating
  http://www.felge.us/BeginGuideCW.htm
  https://elmering.wordpress.com/2011/09/26/basic-cw-operating-procedures/
  http://www.radioqth.net/cwmanual
  http://www.arrl.org/making-your-first-contact
            Have Fun!

## Slide 10: Conducting A QSO – Phone (cont.)
Phonetics
A - Alpha | N - November
B - Bravo | O - Oscar
C - Charlie | P - Papa
D - Delta | Q - Quebec
E - Echo | R - Romeo
F - Foxtrot | S - Sierra
G - Golf | T - Tango
H - Hotel | U - Uniform
I - India | V - Victor
J - Juliet | W - Whiskey
K - Kilo | X - Xray
L - Lima | Y - Yankee
M - Mike | Z - Zulu